# Abbott Court Playground

City of Fall River

ADA Transition Plan

August 2019

200 Portland Street, Boston, MA 02114

www.IHCDesign.org • info@IHCDesign.org

617-695-1225 voice/tty

## Abbott Court Playground

## Background

Abbott Court Playground is located in Fall River between Birch Street (north side) and King Philip Street (south side). Amenities include a basketball court, two (2) baseball fields, two (2) playgrounds a skateboard park and places to sit. On-street parking is available around the park.

## Key Accessibility Issues

### Accessible Routes

The major accessibility issue is the lack of an accessible route that connects all the amenities in the park (basketball court, baseball fields, playgrounds, skateboard park, benches, etc.). Also of concern is the excessive slope at the walkway from the entrance, located on King Philip Street, to the playground.

### Areas of Sports Activity

The major accessibility issue is the lack of accessible routes to the majority of sport activities (including playing areas, spectator seating areas, and dugouts).

### Playgrounds

Major accessibility issues include the lack of a compliant accessible route around the playground located on the north side of the park and a lack of an accessible route to each play component in the playgrounds.

Note: The Massachusetts Architectural Access Board (MAAB) does not consider engineered wood fiber (EWF) to comply with its regulation requiring an accessible route to each play component and around the playground.

## Order of Magnitude Cost Estimates

- Provide an accessible route around the playgrounds and to each play component in the playgrounds (poured in place rubber): $22,087

- Provide an accessible route that connects all elements in the park: $17,124

- Miscellaneous corrective actions: (directional signage, etc.):  $260

Total: $39,471

## Best Practice and Inclusive Design Recommendations

Best practice and inclusive design recommendations include elements that are not required in the standards but may create enhanced experiences for all users.

- IHCD strongly recommends exploring the possibility of an alternative surface to engineered wood fiber (EWF).  Overtime, EWF requires continuous maintenance to ensure the surface is maintained in operable working condition (stable, firm and slip resistant). In addition, when used in combination with other surfaces required for accessible routes to play components in Massachusetts, it will present a challenge to prevent level changes at the transition points between EWF and other surfaces, and to keep the accessible routes clear of EWF.

- Recommend providing handrails on both sides at the stair located on Birch Street. Also, recommend adding contrasting strips at the edge of each step.