# Bank Street Tot Lot

City of Fall River

ADA Transition Plan

August 2019

200 Portland Street, Boston, MA 02114

www.IHCDesign.org • info@IHCDesign.org

617-695-1225 voice/tty

## Bank Street Tot Lot

Year Renovated: 2012

## Background

Bank Street Tot Lot is located at 433 – 371 Bank Street. Amenities include a playground, a blacktop and places to sit. On-street parking is available around the park.

## Key Accessibility Issues

### Accessible Routes

The major accessibility issue is the lack of an accessible route that connects all the amenities in the park (playground, benches, blacktop, etc.).

### Playground

Major accessibility issues include the lack of a compliant accessible route around the playground and lack of an accessible route to each play component.

Note: The Massachusetts Architectural Access Board (MAAB) does not consider engineered wood fiber (EWF) to comply with its regulation requiring an accessible route to each play component and around the playground.

## Order of Magnitude Cost Estimates

- Provide accessible surfaces in the playground to areas around and under play components (poured-in-place rubber): $8,004

- Provide an accessible route that connects all elements in the park: $1,725

Total: $9,729

## Best Practice and Inclusive Design Recommendations

Best practice and inclusive design recommendations include elements that are not required in the standards but may create enhanced experiences for all users.

- IHCD strongly recommends exploring the possibility of an alternative surface to engineered wood fiber (EWF).  Overtime, EWF requires continuous maintenance to ensure the surface is maintained in operable working condition (stable, firm and slip-resistant). In addition, when used in combination with other surfaces required for accessible routes to play components in Massachusetts, it will present a challenge to prevent level changes at the transition points between EWF and other surfaces, and to keep the accessible routes clear of EWF.