# Britland Park

City of Fall River

ADA Transition Plan

August 2019

200 Portland Street, Boston, MA 02114

www.IHCDesign.org • info@IHCDesign.org

617-695-1225 voice/tty

## Britland Park

Year Built: 1975

## Background

Britland Park is located in Fall River at the east end of Wordell Street. Amenities include three (3) basketball courts, two (2) tennis courts, a playground, a soccer field named the Billy Gonsalves Soccer Field, and a comfort station. The comfort station has multi-user men’s and women’s toilet rooms. There is an additional, accessible portable toilet near the soccer field.  Off-street parking is available in a large, paved lot. There is space for approximately 85 cars.

## Key Accessibility Issues

### Accessible Routes

The major accessibility issue is the lack of an accessible route to the basketball courts or the playground. Also of concern is the crack on the route to the tennis court.

### Playground

Major accessibility issues include lack of an accessible route to the playground, lack of an accessible route around the playground, and lack of an accessible route to each play element within the playground.

Note: The Massachusetts Architectural Access Board (MAAB) does not consider engineered wood fiber (EWF) to comply with its regulation requiring an accessible route to each play component and around the playground.

### Toilet Rooms

Major accessibility issues include the lack of a clear depth of 72” in the men’s and women’s accessible compartments and rear grab bars shorter than the minimum length required. Also of concern in the men’s accessible compartment is the door with incorrect swing and flush control not on the open/transfer side. Additional concerns in the women’s accessible compartment include a malfunctioning self-closing hinge and grab bars located lower than the minimum required. Both toilet rooms have lavatories with exposed plumbing and dispensers that protrude into the circulation path and are located higher than the maximum height allowed. In addition, both toilet rooms lack visual fire alarms.

## Order of Magnitude Cost Estimates

- Renovate and provide accessible exterior routes: $1,859

- Provide an accessible route to and around the playground, and to each play component in the playground (poured in place rubber): $ 11,247

- Toilet room renovations: $ 14,174

- Parking lot renovations: $ 5,552

Total: $32,832

## Best Practice and Inclusive Design Recommendations

Best practice and inclusive design recommendations include elements that are not required in the standards but may create enhanced experiences for all users.

- IHCD strongly recommends exploring the possibility of an alternative surface to engineered wood fiber (EWF).  Overtime, EWF requires continuous maintenance to ensure the surface is maintained in operable working condition (stable, firm and slip-resistant). In addition, when used in combination with other surfaces required for accessible routes to play components in Massachusetts, it will present a challenge to prevent level changes at the transition points between EWF and other surfaces, and to keep the accessible routes clear of EWF.

- Recommend providing at least one accessible locker in each toilet room.