# Columbus Playground

City of Fall River

ADA Transition Plan

August 2019

200 Portland Street, Boston, MA 02114

www.IHCDesign.org • info@IHCDesign.org

617-695-1225 voice/tty

## Columbus Playground

## Background

Columbus Playground is located at 36 Wall Street. Amenities include a playground, a basketball court, a baseball field, a bocce court and a pavilion. On-street parking is available around the park.

## Key Accessibility Issues

### Accessible Routes

The major accessibility issues are the lack of a compliant sidewalk (Wall Street), lack of compliant curb ramps at some intersections leading to the park and lack of an accessible route to some elements in the park.

### Areas of Sports Activity

The major accessibility issue is the lack of accessible routes to the area of sport activities (including playing areas and dugouts). Additionally there is a lack of clear floor space at the sideline seating areas.

### Playground

Major accessibility issues include the lack of a compliant accessible route around the playground and lack of an accessible route to each play component. Also of concern, is the lack of a compliant transfer system at some of the ground level play components.

Note: The Massachusetts Architectural Access Board (MAAB) does not consider engineered wood fiber (EWF) to comply with its regulation requiring an accessible route to each play component and around the playground.

## Order of Magnitude Cost Estimates

- Provide compliant curb ramps: $5,728

- Provide an accessible route that connects all elements in the park: $1,624

- Provide an accessible route around the playground and to each play component (poured-in-place rubber): $17,814

- Miscellaneous corrective actions (clear floor space at team seating areas, sidelines and benches, maneuvering clearance at bench, accessible chees table, etc.): $4,250

Total: $29,416*

*Cost to renovate the sidewalk (Wall Street) is not provided.

## Best Practice and Inclusive Design Recommendations

Best practice and inclusive design recommendations include elements that are not required in the standards but may create enhanced experiences for all users.

- Recommend providing detectable warnings at the curb ramps near the park.

- IHCD strongly recommends exploring the possibility of an alternative surface to engineered wood fiber (EWF).  Overtime, EWF requires continuous maintenance to ensure the surface is maintained in operable working condition (stable, firm and slip-resistant). In addition, when used in combination with other surfaces required for accessible routes to play components in Massachusetts, it will present a challenge to prevent level changes at the transition points between EWF and other surfaces, and to keep the accessible routes clear of EWF.