# Public Works Dept. Building

City of Fall River

ADA Transition Plan

September 2019

200 Portland Street, Boston, MA 02114

www.IHCDesign.org • info@IHCDesign.org

617-695-1225 voice/tty

## Fall River Public Works Dept. Building

## Background

The Fall River Public Works Department is located at 10 Lewiston Street. The site includes an office space, a waste processing and a recycling center. Additionally, the site has book drop-offs for donation, and periodically hosts a hazardous waste drop-off day. Other buildings include an apparatus bay, and a road salt and sand silo.

There are two (2) designated accessible parking spaces. The Office area includes a service counter and non-accessible men’s and women’s toilet rooms.

## Key Accessibility Issues

### Parking Lot

Accessibility issues include lack of marked access aisles, identifications signs mounted lower than the minimum allowed and lack the designation “Van-Accessible” at one of the parking spaces.

### Toilet Rooms

The major accessibility issue is the lack of accessible men’s and women’s toilet rooms. Additional accessibility issues at the toilet room include lack of compliant door hardware and lack of compliant designation signs.

### Other Accessibility Issues

- Lack of an accessible service counter.

- Lack of a compliant Hi-Lo drinking fountain for seated and standing users.

- Lack of a compliant threshold (office door).

## Order of Magnitude Cost Estimates

- Renovate toilet rooms: $28,038

- Provide a compliant Hi-Lo drinking fountain: $3,162

- Miscellaneous corrective actions (parking, service counter, doors, etc.): $2,247

Total: $ 33,447