# Desmarais Playground

City of Fall River

ADA Transition Plan

August 2019

200 Portland Street, Boston, MA 02114

www.IHCDesign.org • info@IHCDesign.org

617-695-1225 voice/tty

## Desmarais Playground

## Background

Desmarais Playground is located at the intersection of McGowan Street and County Street in Fall River. Amenities include two (2) playgrounds, a play table and places to sit. On-street parking is available near the park.

## Key Accessibility Issues

### Accessible Routes

The major accessibility issue is the lack of an accessible route that connects all the amenities in the park (playgrounds, benches, etc.).

### Playground

Major accessibility issues include the lack of a compliant accessible route around the playground and lack of an accessible route to each play component. Also of concern is the lack of a compliant transfer system at the playground located on the south side of the park.

Note: The Massachusetts Architectural Access Board (MAAB) does not consider engineered wood fiber (EWF) to comply with its regulation requiring an accessible route to each play component and around the playground.

## Order of Magnitude Cost Estimates

- Provide an accessible route that connects all elements in the park: $6,300

- Provide an accessible route to each play component (poured in place rubber): $4,550

- Miscellaneous corrective actions: (clear floor space at benches, etc.): $136

Total: $10,986*

*Cost to provide a compliant playground is not provided.

## Best Practice and Inclusive Design Recommendations

Best practice and inclusive design recommendations include elements that are not required in the standards but may create enhanced experiences for all users.

- IHCD strongly recommends exploring the possibility of an alternative surface to engineered wood fiber (EWF).  Overtime, EWF requires continuous maintenance to ensure the surface is maintained in operable working condition (stable, firm and slip resistant). In addition, when used in combination with other surfaces required for accessible routes to play components in Massachusetts, it will present a challenge to prevent level changes at the transition points between EWF and other surfaces, and to keep the accessible routes clear of EWF.

- Recommend providing a crosswalk near the entrance to the park (intersection of Pleasant Street and County Street).

- Recommend making sure the correct address of the park is on the City’s website.