# Dumont Park

City of Fall River

ADA Transition Plan

September 2019

200 Portland Street, Boston, MA 02114

www.IHCDesign.org • info@IHCDesign.org

617-695-1225 voice/tty

## Dumont Park

## Background

Dumont Park is located along Russell Brogan Boulevard. Amenities include three (3) little league baseball fields, a concession stand, a single-user toilet room and bleachers. There is not a designated parking lot.

## Key Accessibility Issues

### Accessible Routes

The major accessibility issue is the lack of accessible routes that connect all amenities in the park.

### Areas of Sports Activity

The major accessibility issue is the lack of accessible routes to the area of sport activity including dugouts and spectator seating.

### Concession Stand

Accessibility issues include lack of an accessible single-user toilet room and the service counter at the concession stand is higher than the maximum allowed.

## Order of Magnitude Cost Estimates

- Provide an accessible route that connects all amenities in the park (sport activity, sideline seating, concession stand, etc.): $16,248

- Provide an accessible single-user toilet room: $18,627

- Miscellaneous Corrective Actions (clear floor space at spectator seating, accessible counter at concession stand, etc.): $1,088

Total: $35,963

## Best Practice and Inclusive Design Recommendations

Best practice and inclusive design recommendations include elements that are not required in the standards but may create enhanced experiences for all users.

- Until the single-user toilet room is made accessible, recommend providing accessible portable toilets near the fields.

- Recommend exploring the possibility of providing accessible parking spaces near the park.

- Recommend providing sidewalks at the streets leading to Dumont Park.