# Fire Museum/Animal Control

City of Fall River

ADA Transition Plan

August 2019

200 Portland Street, Boston, MA 02114

www.IHCDesign.org • info@IHCDesign.org

617-695-1225 voice/tty

## Fall River Fire Museum/Animal Control

Year Built: 1873		Year Renovated: 2019 (Ongoing)

## Background

The Fall River Fire Museum/Animal Control is located at 1181 North Main Street. The building is an antique firehouse which has been repurposed as a Fire Museum and the headquarters for the Fall River Animal Control Center. The Fire Museum is in the process of being renovated, and currently is not open to the public. Amenities include a variety of Fall River Fire Department memorabilia, three (3) antique fire trucks of various vintages, and an inaccessible single-user toilet room. The Animal Control’s public amenities include a lobby and an inaccessible single-user toilet room.

The building is a single-story, with a non-public basement used for storage. The Fire Museum is on the north side of the building, and the Animal Control on the south. There are two (2) entrances - one for each facility – on the west side of the building. There is an additional exit (south side) in the Animal Control that is not currently used.

The building has limited parking, with three (3) spaces at the front of the building, as well as an unpaved lot located on the west end of the property with room for approximately 10 parking spaces. This lot is labeled as being exclusively for the Animal Control visitors. There are no accessible spaces at the Fire Museum or Animal Control.

## Key Accessibility Issues

### Fire Museum

Major accessibility issues at the Fire Museum include:

- Excessive change in level at the vestibule entrance to the Fire Museum.

- Lack of accessible parking spaces.

- Lack of surface that is stable firm and slip-resistant due to deteriorated flooring.

- Lack of an accessible single-user toilet room.

Note: IHCD staff was informed of pending renovations to the toilet room.

### Animal Control

Major accessibility issues at the Animal Control include:

- Lack of a compliant accessible parking space at the designated lot for Animal Control patrons.

- Lack of an accessible single-user toilet room, lack of door hardware that does not require tight pinching, grasping, or twisting of the wrist and lack of compliant designation signage at the single-user toilet room.

- Lack of an accessible entrance (the main entrance has an 11” high step).

Note: IHCD recommends exploring the possibility of making the entrance located on Brownell Street, the accessible entrance to the Animal Control’s facilities.

## Order of Magnitude Cost Estimates

### Fire Museum

- Provide an accessible single-user toilet room: $18,453

- Miscellaneous corrective actions (van accessible parking space, change in level, etc.): $754

Total: $19,207*

### Animal Control

- Provide an accessible route (to the entrance located on Brownell Street): $1,913

- Provide an accessible single-user toilet room: $18,453

- Provide compliant door hardware: $1,089

- Miscellaneous corrective actions (van accessible parking space, directional and designation signs, etc.): $1,468

Total: $22,923*

*Cost does not include the renovations to flooring surfaces.