# Stanley Fire Station

City of Fall River

ADA Transition Plan

September 2019

200 Portland Street, Boston, MA 02114

www.IHCDesign.org • info@IHCDesign.org

617-695-1225 voice/tty

## Stanley Fire Station

Year Built: 1951

## Background

The Stanley Fire Station is located at 229 Stanley Street and is one of the six (6) fire stations that encompass the Fire Department in Fall River. The building is a two (2) story building with firefighters living area on the second floor.

The main entrance to the fire station is on Stanley Street – the entrance has minor accessibility issues. There are two (2) non- accessible emergency exits, one on the west side, and another on the east side of the building.

The parking lot is located on the south side of the building, there are twelve (12) parking spaces but no accessible spaces.

## Key Accessibility Issues

### Entrances and exits

Accessibility issues include lack of a beveled threshold at the main entrance and lack of accessible exits.

### Signage

The major accessibility issue is the lack of tactile egress signs (braille and raised characters) at the emergency exits and lack of the illuminated sign with the International Symbol of Accessibility (ISA) at the main entrance.

### Toilet Rooms

The major accessibility issue is the lack of an accessible single-use toilet room.

## Order of Magnitude Cost Estimates

- Renovate toilet room: $18,453

- Miscellaneous corrective actions (parking, signs, threshold at door, etc.):  $1,235

Total: $19,688