## Introduction

The Institute for Human Centered Design (IHCD) has prepared this report on behalf of the City of Fall River as part of the City’s on-going effort to assess the current level of ADA compliance in programs, services and activities and City-owned facilities. In preparing for this report, IHCD teams surveyed the City’s portfolio of facilities and properties that were included in the Request for Proposal.

The building facility set includes nineteen (19) public buildings – including six (6) Fire Stations and four (4) Senior Centers*. The accessibility survey of those facilities includes all the spaces where the City offers programs, services and activities to members of the public. The outdoor facility set includes twenty-five (25) parks/outdoor areas. The accessibility survey of those spaces encompassed elements such as accessible routes, walking surfaces, slopes, picnic tables, play areas and recreational areas.

*Note: Please note that since the day of the survey by IHCD team, the Flint Senior Center located on Pleasant Street is no longer utilized. That Center now has a new location on Alden Street.

In addition, twenty-one (21) polling places were also included in this assessment. The accessibility survey of those facilities includes accessible routes, accessible entrances, the area where the voting takes place and the toilet rooms associated with the voting area.

IHCD submitted separate reports for each facility that was surveyed. To assist in prioritizing accessibility improvements to ensure compliance with the ADA Title II, each of the building and outdoor area reports include an overview that identifies the most substantial accessibility issues and order of magnitude cost estimates for corrective action. Additionally, a detailed catalog that supplements the ADA Self-Evaluation narrative overview is also included. The catalog provides element-by-element photos of compliance issues, location and measurements - when applicable - at each assessed facility accompanied by recommendations and cost estimation for each accessibility issue.

In addition, a spreadsheet of priorities for corrective action organized by type of building and including order of magnitude costs was provided to the City. When the City presents findings and recommendations to the community and receives feedback, some recommendations may need cost adjustment.  These spreadsheets are a capital planning and budgeting tool - the “ADA Transition Plan” and is intended as a long-term tool to update as work is completed. The City should make a good effort to complete the work in a reasonable time (IHCD recommends a five

to ten-year period). Together, the ADA Self-Evaluation and ADA Transition Plan will enable the City to make substantial progress in meeting its ADA responsibilities. The recommendations for corrective action on policies and procedures of the ADA Self-Evaluation are not included in the ADA Transition Plan since that is limited to capital accessibility issues. But they are a blueprint for meeting compliance responsibilities other than capital expenses.

IHCD also submitted a complete assessment of the City’s policies, practices and procedures.

The ADA administrative requirements help ensure that the needs of people with disabilities are addressed in all services, programs and activities that the City operates. 
See the complete summary in Part B – Evaluation of Non – Discriminatory Policies and Practices in Programs, Services and Activities report.

A complete website accessibility report that provides information about website accessibility issues and recommendations for corrective measures was also submitted.

Most City-owned facilities recently altered or renovated are substantially accessible and meet most architectural requirements.  Continued facility alterations, and/or renovations will significantly reduce barriers and realize the City’s commitment to inclusion and equal rights. In the meantime, the greatest problems posed by existing barriers can be ameliorated by establishing policies and procedures to accommodate members of the community with disabilities. It is worth noting that the City has taken several significant steps in this direction:

- The City of Fall River has hired a consultant (IHCD) to undertake its ADA self-evaluation (as basis for the City’s Transition Plan).

- The City of Fall River has an ADA Coordinator in place.

- The City has adopted a Public Notice Policy (posted on the City’s website).

- The City has developed a Grievance Procedure (posted on the City’s website).

IHCD’s review and recommendations of the City-owned facilities was based on compliance with the 2010 ADA Standards if not compliant with the 1991 ADA Standards and/or 521 CMR of the Massachusetts Architectural Access Board. Best practice and inclusive design recommendations were also provided for each property. Inclusive design recommendations include elements that are not required in the accessibility standards but may create enhanced experiences for all users.

Many key facilities and outdoor areas are generally usable by people with disabilities but are not in full compliance with current accessibility requirements. The Government Center, for instance, provides access to many programs and can be accessed by most people because the building features an accessible entrance, accessible toilet rooms, and has accessible routes through the building. Yet some of the key areas such as the Hearing Room lacks an accessible route to the lower area and service counters at a few departments are higher than the maximum allowed, a key component to access some of the services provided by the City. The City Library is another example of a facility that provides access to most programs, yet the facility lacks fully accessible multi-user toilet rooms which many individuals with mobility disabilities require.

The City may comply with the requirements of Title II of the ADA through means such as reassignment of services to accessible buildings or delivery of services at alternate accessible sites. The City may also comply with the requirements by renovation or alteration of existing facilities and/or construction of new facilities, or any other methods that result in making the City’s services, programs or activities readily accessible to and usable by individuals with disabilities. Note that a public entity is not required to make structural changes in existing facilities where other methods are effective in achieving compliance with this section.

In choosing among available methods for meeting the requirements of the ADA, the City of Fall River shall give priority to those methods that offer services, programs, and activities to qualified individuals with disabilities in the most integrated setting appropriate.

In order to comply with the program accessibility obligations the City of Fall River should consider:

- Relocation of its programs, services and activities within current facility

Often the simplest solution is for the City to use what it already has in place. IHCD strongly recommends the relocation of programs, services and activities to accessible locations within the facility.

- Relocation of its programs, services and activities to another facility

When it is not possible to relocate them within the current facility, program, services, and activities should be relocated to an accessible facility.

- Renovation/alteration of its facilities to ensure access to programs, services and activities

The City may consider the renovation of its facilities to ensure that the programs, services and activities are offered in the most integrated seating possible.

Note that any corrective actions needed to ensure program accessibility must comply with the requirements of the 2010 ADA Standards and/or 521 CMR.

Furthermore, when doing alteration/renovation, keep in mind that an alteration that decreases the accessibility of a building bellow the requirements for new construction at the time of the alteration is prohibited.

To determine which buildings must be made accessible, the City should consider:

- How to provide the program in the most integrated setting appropriate;

- The locations where the activities are offered;

- Which facilities are accessible and to what extent.

## Key Recommendations for the Building Facilities:

- Ensure there is an accessible route from all arrival points to those areas in the building where the programs, services and activities are provided.

This recommendation applies particularly to the fire stations where school tours are being offered. Currently, many of the accessible routes to enter the stations are through the bay doors.

- Ensure that fully accessible toilet rooms are provided in the building. Where it is technically infeasible to provide accessible multi-user toilet rooms provide an accessible single-user toilet room in the same area as the existing multi-user toilet rooms.

As mentioned before, fire stations offer school tours yet the majority of the stations don’t have accessible toilet rooms.

- Ensure that where the programs, services or activities are offered there is a sufficient number of accessible features (accessible counters, accessible work surfaces, etc.).

Particular attention should be giving to the Government Center building and the Police Department where key programs are being offered to the community.

- If audible communication is integral to the use of the space, provide a compliant assistive listening system.

This should be a priority at the hearing room at the Government Center building and the Community Room at the Police Department.

In addition, at the Police Department, ensure that the telephones provided in the visiting booths are equipped with volume control on both sides of the window.

When looking at the outdoor facilities, the City of Fall River needs to ensure that a sufficient number of locations are accessible. For instance, the City of Fall River offers a variety of experiences at its parks/outdoor areas e.g., playgrounds, picnic areas, playing fields, etc.  The City needs to make sure that a sufficient number of each type of these facilities is accessible. The City also needs to keep in mind that each unique program needs to be accessible.

The City should ensure that privately owned and/or operated facilities on City property are in compliance with the ADA. Furthermore, the City should ensure that the baseball leagues are operated in a manner that enables the City to meet its Title II obligations.

## Key Recommendations for the Outdoor Facilities:

- Ensure there is an accessible route to all elements in the park/outdoor space (baseball fields, basketball courts, playgrounds, picnic areas, toilet facilities, etc.).

- Ensure there is a clear floor space adjacent to the bench at team seating areas and spectator seating areas.

Diagram of clear floor space at team seating area

- Ensure that accessible routes are provided to and around playgrounds; in addition, ensure that an accessible route is provided in the play area to all play components.

The majority of the playgrounds have Engineered Wood Fiber (EWF) as surface. Note that the Massachusetts Architectural Access Board (MAAB) does not consider Engineered Wood Fiber (EWF) to comply with its regulation requiring an accessible route to and around playground equipment.

- Ensure that a certain number of amenities (at least 5%) in the parks/outdoor spaces are accessible (e.g., picnic tables, service counters at concession stands, etc.).

## Key Recommendations for the Polling Facilities:

IHCD proposed recommendations are for permanent solutions that provide increased accessibility at all times. While permanently removing architectural barriers is preferable, the City can choose to provide some low-cost, temporary solutions that can provide access to the polling place for people with disabilities on Election Day.

- If parking is provided:

  - Ensure accessible parking spaces are provided. If there is no accessible parking ensure at least one temporary accessible parking space is provided.

  - Ensure accessible parking spaces are located in a level area with no steep slopes and on the shortest accessible route from the parking to the accessible entrance to the polling place.

- Ensure a 32” minimum width is provided at the door leading to the voting area.

- Ensure a 36” minimum width is provided at the accessible route in and through the voting area.

- Ensure a 30” minimum by 48” minimum clear floor space is provided in at least one accessible voting station or booth to allow a voter using a wheelchair or other mobility device to approach, maneuver, and leave the voting station.

- Ensure floor surfaces are stable, firm, and slip resistant.